## Slide 1
Sewmehon E.
ARM Microprocessor - Interrupts and Timers

## Slide 2
2. Interrupts
4. Conclusion
3. Timers
1. Introduction
CONTENTS

## Slide 3
Introduction
The ARM microprocessor includes crucial functionalities such as interrupts and timers, which help manage real-time operations efficiently. This document provides an in-depth explanation of these concepts, their functionalities, and their applications in embedded systems.

## Slide 4
An interrupt is a signal sent to the processor to notify it of an event requiring immediate attention. The processor temporarily halts execution, invokes an Interrupt Service Routine (ISR) to handle the event, and resumes its prior execution once the event is handled.
Interrupts

## Slide 5
Active: The ISR is currently executing the interrupt.
Interrupts can exist in the following three states:
Inactive: No conditions have been met to generate an interrupt.
Pending: Conditions for generating the interrupt are met, but ISR has not been executed yet.
Once the event is handled, the interrupt state returns to inactive.
Interrupt States

## Slide 6
The hardware implementation of interrupts involves multiple components:
Interrupt Trigger: The hardware event that generates the interrupt via an electrical signal.
Interrupt Vector Table (IVT): A table storing the addresses of all ISRs in memory.
Interrupt Masking: Allows disabling of interrupts selectively to avoid conflicts.
Interrupt Components
Interrupt Source: Any peripheral (ADC, Timer, GPIO, UART) that triggers an interrupt.
Interrupt Controller: A peripheral that manages the interrupts.

## Slide 7
A high-priority interrupt can preempt a low-priority interrupt's execution.
Interrupts are assigned numerical priorities.
Higher-priority interrupts are serviced before lower-priority ones.
Interrupt controllers utilize flags to signal event occurrences:
Nested Vector Interrupt Controller (NVIC): Manages prioritization and nesting of interrupts in ARM microcontrollers.
Interrupt Flags and Priorities
Priority Levels:
Interrupt Enable Flag: Determines whether the processor acknowledges and services an interrupt.

## Slide 8
The ISR corresponding to the interrupt is fetched from the Interrupt Vector Table.
The current state of the CPU is saved.
The program resumes from where it was interrupted.
Software Handling of Interrupts
The ISR is executed to handle the event.
When an interrupt occurs, the following steps are executed:
Once execution is complete, the saved CPU state is restored.

## Slide 9
Real-time processing: Used in critical real-time applications such as robotics and automation.
Power-saving: Enables processors to remain in low-power mode and wake up only when an interrupt occurs.
Applications of Interrupts
Event-driven execution: Improves efficiency by responding to external triggers instead of continuous polling.

## Slide 10
A timer is a hardware peripheral used to measure time and generate precise delays. ARM-based microcontrollers, such as MSP432, feature Timer32, a 32-bit timer.
Timers

## Slide 11
4
2
1
5
3
Counting external events.
Timers perform the following key functions:
Timer Functions
Generating time delays.
Operating independently of the CPU.
Scheduling periodic tasks in real-time operating systems (RTOS).

## Slide 12
One-Shot Mode: The timer counts down once and stops.
PWM (Pulse Width Modulation) Mode: Used for controlling motors and LED brightness.
Timers operate in two main modes:
Capture Mode: Captures external events such as button presses.
Timer Operation Modes
Periodic Mode: The timer reloads its count value after reaching zero and continues running.

## Slide 13
Prescaler: Divides the input clock frequency to achieve longer delays.
Clock Source: Provides the timing reference.
Timer Components
Timers consist of:
Compare Register: Holds the predefined value to trigger an event.
Flag Register: Signals when the timer reaches the predefined value.
Counter Register: Stores the countdown value.

## Slide 14
2
3
6
1
4
5
Delay Generation:
Timers generate PWM signals to control motor speed or LED intensity.
Timer Example Applications(1)
Speed Calculation: An IR sensor connected to a vehicle's wheel generates pulses. A counter counts these pulses to measure speed.
PWM Signal Generation:
Given an 8-bit timer with a frequency of 40Hz, a required delay of 100ms can be achieved by setting the compare register to 4.
Since 1 pulse = 25ms, when the counter reaches 4, 100ms delay is achieved.

## Slide 15
1
2
Real-Time Clock (RTC) Implementation: Timers help in implementing an RTC by keeping track of seconds, minutes, and hours.
Example: A 50% duty cycle PWM signal means the output is ON for half the period and OFF for the other half.
Timer Example Applications(2)

## Slide 16
Conclusion
Interrupts and timers are fundamental in embedded systems, enabling efficient handling of real-time events. Proper understanding of these components ensures optimized performance of microcontroller-based applications. The ARM microcontroller's NVIC system enhances interrupt handling, while timers provide critical functionality for event scheduling, delay generation, and signal processing.

## Slide 17
Thank You